## Slide 1: Stakeholder meeting- AutoRef
01/03/2024
Quinten Swaan, Project Manager
Department of Mathematics and Computer Science, EngD. Mechatronic Systems Design

## Slide 2: Agenda
  Planning
  Risks
  Validation
  Sensor system
  Ball out of play
  Last touch
  Summary
  14:00 – 14:05
  14:05 – 14:10
  14:10 – 14:20
  14:20 – 14:30
  14:30 – 14:40
  14:45 – 14:55
  14:55 – 15:00
Goal: update on progress.

## Slide 3: Deliverables
Performance
Objectivity
Accurate
Robustness
Real-time
Consistent decisions
Progress
Continuity
Communication
Safety
Follow RoboCup MSL rules
Showing proof
Sending decisions
Adaptability
Challenging
Personal learning goals
Interests
Mission: “To observe the match and make autonomous, unbiased decisions based on the soccer robot rules that can be communicated to teams and viewers. ”

## Slide 4: Deliverables
  Which team touched the ball the last time before the ball went out of field while the game was in play?
  Communication to the referee about the decision above.
  Motivation
Difficult for human referees
Objectivity
Challenging and interesting
Challenging
New feature
Progress
Building on BOOP
Continuity
Assistant to referee
Communication

## Slide 5: System context diagram
System
RefBox
BOOP?
Human referee
Decision
Game state
RoboCup MSL Rules & Regulations
Developers

## Slide 6: Deliverables
  End presentation.
  Technical report.
  Codebase.
  Demo, showcasing our system.

## Slide 7: Risks
Severity
Occurrence
Trust
Bias
Robustness
Security
Sensing accuracy
Edge cases
Validation and verification
Implementation
Robustness
Bias
Security
Edge cases
Trust
Validation and verification
Implementation
Sensing accuracy

## Slide 8: Work Breakdown Structure
WBS
Concept Approval
System Architecture Review
System Implementation
Literature Review
Feasibility Study
Rules Book Summarization
Decision Stories
Decision Trade-off Matrix
Requirements and Specifications Review
User Needs
Requirements Definition
Extract Technical Specifications
Defining Project Scope
System Functionalities
Preliminary Design Review
Critical Design Review
Subsystems Deployment
Subsystems Integration
Verification & Validation
Verification Review
Validation Review
Documentation Approval
Presentation & Demonstration
Project Closure
Project Delivery

## Slide 9: Planning

## Slide 10: Functional requirements and specifications
Arjun, Joseph and Naheed

## Slide 11: Functional requirements
Ground Truth
Time for Decision Making
Distinguish Last Touch
Detect Ball out of Field
Change in Game State
Communication to Referee
Frames per Second
Zero-Trust
Time Stamps
Transparency

## Slide 12: Functional requirements
Time for Decision Making
Distinguish Last Touch
Maximum Distance Error
Operational Time
Change in Game State
Communication to Medium
Live data streaming
Zero-Trust
Time Stamps
Transparency

## Slide 13: Ground truth
The stakeholders expressed that we stick to the order of things, processes then requirements then specifications and then solutions. And in order to define the requirements, we need to set the stage for a ground truth.
For the ground truth, it was requested that we rely on how a human referee makes decisions. But a human referee makes decisions in the real world which is not virtual.
Why do I take the time to dedicate an entire slide to ground truth? It is because we had to delve into the solution space on a cursory level to decide on how to define a touch, but there is a virtual world in which a touch is defined the same way it is in the real world.
Assume that we virtualize the real world, and even though we don’t need to actually do it, it’s good to have it as a sort of thought experiment, and it can be done with the OptiTrack and photogrammetry.
Now we use this thought experiment as the basis for what follows.

## Slide 14: Time for decision making
The Assistant Referee (AR) can make the combined decision (ball out of play and last touch) in real-time in less than 1 second.
Reason: Based on discussion with Tech United and requirements of the previous year.

## Slide 15: Distinguish last touch
AR can distinguish who touched the ball last with desired accuracy at least as good as human, 70% correct decision
References:
  55% to 85% accurate on average for a match,
  Brazilian referees by De Oliveira et all (2011),
  Physical Performance and Decision Making in Association Football Referees: A Naturalistic Study

## Slide 16: Maximum distance error
AR is allowed a ±1.5cm error in distance between objects
Reason: The Goal-Line Technology has an accuracy of ±1.5 cm.

## Slide 17: Operational time
AR must ensure operational time of 2 hours.
Reason: The Goal-Line Technology has an operational time of 6 hours for a 1.5 hour game, which yields a safety factor of 4, incorporating the same here, we get 2 hours.

## Slide 18: Change in game state
The latency of the signal which reflects the change in game state to the AR should be 150ms maximum.
Explanation: Suppose that the referee stops the game using the interface provided by RefBox. The signal should reach the AR within 150ms.
To reduce the false detection of the decision, if the ball is already out of play.

## Slide 19: Communication to Medium
AR can communicate the decision it made to the medium in 250ms.
Reason: This is the human reaction time to a visual stimulus.

## Slide 20: Live data streaming
AR should receive inputs from the playing field with a minimum frequency of 20 frames per second. (20 Hz)
Reason: The number is taken from the previous year’s document.

## Slide 21: Zero-trust
AR should receive data from independent sensors and not from the robots playing the match.
Reason: We don’t trust the data from the teams.

## Slide 22: Time stamps
The sensors the AR receives the data from must come with a timestamp, else a timestamp has to be associated with them.
Reason: Transparency for fair decision-making. Also, it’s not unreasonable to expect a timestamp.

## Slide 23: Transparency
AR should be able to walk us through the decision making process if questioned.
Reason: First, since the project is in the software domain, a well-commented code should do that. Second, it is supposed to be fair to the participating teams.

## Slide 24: THANK YOU
Arjun, Joseph and Naheed

## Slide 25
Validating the functional requirements
Real-world scenarios
Comparison to human referees
Ground truth
Statistical Analysis
Validation objectives

## Slide 26
Initial Preparations
System Setup
Independence Verification
Real-world Scenario
2 vs. 2 match at Tech United field
Human referees assisted by the autoref system
Edge cases
Input Data Validation
Recording and ground truth analysis
Setup

## Slide 27
Statistical Metrics
Accuracy
Confusion Matrix
F1 Score
Comparison to Human Referee
Human-like Decision Making
Overall Performance
Analysis methods overview

## Slide 28
System architecture

## Slide 29: Summary